User's Guide

# ODP Application
# Initialization
## Startup
## Shutdown
## Views
### Logical view
### Application View
Packet input
Pre processing

Classification

Input Queuing

Delivery Scheduling

Parallel CPU
processing

Co processing

HW
SW
DPI
Crypto
Output Queuing
Post Processing
Packet Output

Buffer Management

Loopback

Inline Ipsec
decryption

Buffer alloc
Buffer alloc / free
Buffer free
Re-classification
Inline Ipsec
encryption

HW close to SW
### System View
Crypto
IPsec
Timer
PktIO
PktIO
lookup
Shaper

# General usage of ODP API, including error handling
## Scheduler
### Configure the scheduler
## Queues
### Atomic

Scheduler

Queues
Atomic queues

### Ordered
Ordered queues ensure that the sequencing at the output is identical to that of the input

Scheduler

Cores
Cores
Queues
Ordered queues

6
7
3

1
2
1
5
3

4

4

2
### Parallel
Parallel queues
### Queue Groups

Scheduler

Cores
Cores
Queues
Parallel queues

Queue groups

Scheduler

Cores
Queues
Queue group

A
A
B
B
## Events
Event is a thing that can be transmitted through queues. Event gives you the event type - nothing more. User needs to convert the received event according to its event type ...
buf = odp_buffer_from_event(event);
.. to access the information
my_msg = odp_buffer_addr(buf);
Buffer gives you the minimal support for transferring bytes through queues. Some events, like timeouts, may have only metadata (not variable sized user data).
## Error Handling

## Error Number
## Synchronization
## Timers
Timeouts are a primary event type, just like buffers and packets. How they are implemented is platform specific.
The timeouts must have the event type ODP_TYPE_TIMEOUT.
## At application start
Create a timer pool with required minimum resolution and and max number of supported (simultaneous) timers. An implementation can thus allocate all necessary resources in advance with no risk for intermittent resource failures during operation.
Specify drift requirements? (Can the timer service provide different implementations with different drift characteristics?) Or is drift requirements covered by the user-defined timer resolution? Allow drift within one user-defined tick but not more than that.

Timer pool creation is not limited to application start, one can imagine use cases where timer pools are created and destroyed throughout the lifetime of the application.
## When a flow/connection is set up or an interface is attached
Allocate (create) timers associated with the parent resource (e.g. flow/connection/interface). Allocate (reserve) all necessary resources for those timers. This may fail and return an error, this will likely lead to failure of the setup of the parent which can be propagated up and handled on a higher level. When all resources have been allocated, the timers can be armed (started).
## When timers are explicitly set or reset
Set and reset of timer must always succeed (immediately or later), in the general case applications (representing the above use cases) can not handle failure without having to partially or totally degrade service (e.g. abort connection). The exception is when resetting a timer whose timeout is in the process of being delivered to the user, such timers can be (re-)set later when the timeout have actually been received by the user. The user should be able to adjust the timeout period, negating the time elapsed before the timeout was received.
## When a resource is torn down
When a resource is torn down (because of some expired timer or because of signaling), all timers are cancelled and the timeouts returned, either directly (synchronously) or (asynchronously) through the specified queue (if the timer had already expired). Internal timer resources are reclaimed. Buffers allocated by the user should be freed by the user. A phased approach where timers are cancelled, any enqueued timeout buffers are received and finally the timers are freed is recommended for reliable operation.
## When timers expire
When timers expire their associated timeouts are enqueued so that they (at some future time) can be received by the client. The expiration and enqueueing is an asynchronous event which cannot directly be observed by the client. This may happen after the "global" expiration clock that the client requested, this can be an effect of the implementation (missing accuracy) or system load (higher priority processing delays timer service) or for any other reason. Timeouts for expired timers are only guaranteed be delivered *eventually* (whether the client actually receives them is the responsibility of the client) but the actual timing is "best effort". The actual quality is dependent on the timer service implementation and system load.

## Packets
### Usage of functionality for processing of packets
### - Packet flow via the classifier
### - Packet data manipulation
### - Packet traffic shaping

## Packet io

PktIO

Default Q
Scheduler
## Buffers
A buffer is a simple block of memmory